FPV 监视器

使用说明书

重要安全说明：

- 合用前请詊细阅读本产品使用指南

- 请詊细阅读注意事项

产品简介：

- 高分辨率：800*480

- 高亮度：400cd/㎡

- 高对比度：500：1

- 可选双模块

- 外观说明

1       2      3    4      5

- 调整菜单选项

- 用于调出菜单与主菜单选择

- 调整菜单选项

- A,B模块选择

- 电源开/关

1    2       3              4                           5

- AV OUT:视频输出接口

- AV IN ：视频输入接口

- 不使用

- 支架接口

- DC12V：12V电源接口

1

、、

- 天线

- 电池接口：3S

- 安装接口

- 拔码天关

- FPV接收信号

1.频率表

| 频道 | CH1 | CH2 | CH3 | CH4 | CH5 |
| --- | --- | --- | --- | --- | --- |
| A 组 |
| 5740 | 0 | 0 | 0 | 1 | 1 |
| 5760 | 1 | 0 | 0 | 1 | 1 |
| 5780 | 0 | 1 | 0 | 1 | 1 |
| 5800 | 1 | 1 | 0 | 1 | 1 |
| 5820 | 0 | 0 | 1 | 1 | 1 |
| 5840 | 1 | 0 | 1 | 1 | 1 |
| 5860 | 0 | 1 | 1 | 1 | 1 |
| B组 |
| 5725 | 0 | 0 | 0 | 0 | 0 |
| 5745 | 1 | 0 | 0 | 0 | 0 |
| 5765 | 0 | 1 | 0 | 0 | 0 |
| 5785 | 1 | 1 | 0 | 0 | 0 |
| 5805 | 0 | 0 | 1 | 0 | 0 |
| 5825 | 1 | 0 | 1 | 0 | 0 |
| 5845 | 0 | 1 | 1 | 0 | 0 |
| 5865 | 1 | 1 | 1 | 0 | 0 |
| C组 |
| 5733 | 0 | 0 | 0 | 1 | 0 |
| 5752 | 1 | 0 | 0 | 1 | 0 |
| 5771 | 0 | 1 | 0 | 1 | 0 |
| 5790 | 1 | 1 | 0 | 1 | 0 |
| 5809 | 0 | 0 | 1 | 1 | 0 |
| 5828 | 1 | 0 | 1 | 1 | 0 |
| 5847 | 0 | 1 | 1 | 1 | 0 |
| 5866 | 1 | 1 | 1 | 1 | 0 |
| D组 |
| 5705 | 0 | 0 | 0 | 0 | 1 |
| 5685 | 1 | 0 | 0 | 0 | 1 |
| 5665 | 0 | 1 | 0 | 0 | 1 |
| 5645 | 1 | 1 | 0 | 0 | 1 |
| 5885 | 0 | 0 | 1 | 0 | 1 |
| 5905 | 1 | 0 | 1 | 0 | 1 |
| 5925 | 0 | 1 | 1 | 0 | 1 |
| 5945 | 1 | 1 | 1 | 0 | 1 |

2 拔码示意图

CH1:5740    CH2: 5760   CH3: 5780   CH4: 5800

CH5 : 5820     CH6: 5840   CH7:5860   CH8:5880

CH1:5725   CH2: 5745   CH3:5765   CH4:5785

CH5 : 5805    CH6: 5825   CH7:5845   CH8: 5865

CH1:5733   CH2: 5752    CH3: 5771   CH4: 5790

CH5:  5809   CH6: 5828   CH7: 5847   CH8:5866

CH1: 5705   CH2 :5685   CH3:5665   CH4: 5645

CH5:  5885    CH6: 5905   CH7:5925   CH8:5945

3 无线信号接收天线

- 将5.8G天线（蘑菇天线，平板天线）与天线接口连接

- 拔码开关信号与发射器信号一致，即可接收

4 配线说明

- 视频输出线

5 菜单设置

- 通电后按电源天关键打开

- 按选择模块A或B

6 附件

标配：

- 遮阳置    1个

- 电源DC线  1条

- AV线       1条

- 电池扣板    2个

- 5.8G天线4DB  2根（单模块1根）

选配：

- 5.8G 4DB天线

- 5.8G 蔴菇天线

- 5.7G 平板天线

- 热靴支架

8 主要参数

| 显示屏 | 7”LED背光 |
| --- | --- |
| 分辨率 | 800*400 |
| 亮度 | 400cd/㎡ |
| 对比度 | 500：1 |
| 可视角度 | 140°/120° |
| 输入电压 | DC7-16V |
| 屏幕比例 | 16：9 /4：3 |
| 电流 | 450mA |
| 功耗 | ≤6W |
| 尺寸 | 186*127*23（mm） |
| 重量 | 380 |

9 常见问题解答

| 故障现像 | 问题分析 |
| --- | --- |
| 无图象 | 检查电源输入和连线 |
| 只有黑白图像 | 亮度，对比度及色度是否适当 |

FPV Monitor

Manual

Important Safety Notice：

- Please look the manual through carefully before using.

- Please read the matters needing attention carefully

Specifications：

- High Resolution：800*480

- High Brightness：400cd/㎡

- High Contrast：500：1

- Dual Modules to choose

- Appearance Illustration

1       2      3    4      5

- Adjusting menu seetings

- Used for calling out the choosing of menu and the main menu

- Adjusting menu settings

- Selection of Module A or Module B

- Power on / off.

1    2       3              4                           5

- AV OUT: Output connector of Video

- AV IN ：Input connector of Video

- None

- Connector of the stand

- DC12V：Power Connector (12V)

1

、、

- Antenna

- Battery Conncetor：3S

- Installation Conncetor

- Dial-up switch

- FPV Signal Receiving

1.Frequency List

| Channel | CH1 | CH2 | CH3 | CH4 | CH5 |
| --- | --- | --- | --- | --- | --- |
| Group A |
| 5740 | 0 | 0 | 0 | 1 | 1 |
| 5760 | 1 | 0 | 0 | 1 | 1 |
| 5780 | 0 | 1 | 0 | 1 | 1 |
| 5800 | 1 | 1 | 0 | 1 | 1 |
| 5820 | 0 | 0 | 1 | 1 | 1 |
| 5840 | 1 | 0 | 1 | 1 | 1 |
| 5860 | 0 | 1 | 1 | 1 | 1 |
| Group B |
| 5725 | 0 | 0 | 0 | 0 | 0 |
| 5745 | 1 | 0 | 0 | 0 | 0 |
| 5765 | 0 | 1 | 0 | 0 | 0 |
| 5785 | 1 | 1 | 0 | 0 | 0 |
| 5805 | 0 | 0 | 1 | 0 | 0 |
| 5825 | 1 | 0 | 1 | 0 | 0 |
| 5845 | 0 | 1 | 1 | 0 | 0 |
| 5865 | 1 | 1 | 1 | 0 | 0 |
| Group C |
| 5733 | 0 | 0 | 0 | 1 | 0 |
| 5752 | 1 | 0 | 0 | 1 | 0 |
| 5771 | 0 | 1 | 0 | 1 | 0 |
| 5790 | 1 | 1 | 0 | 1 | 0 |
| 5809 | 0 | 0 | 1 | 1 | 0 |
| 5828 | 1 | 0 | 1 | 1 | 0 |
| 5847 | 0 | 1 | 1 | 1 | 0 |
| 5866 | 1 | 1 | 1 | 1 | 0 |
| Group D |
| 5705 | 0 | 0 | 0 | 0 | 1 |
| 5685 | 1 | 0 | 0 | 0 | 1 |
| 5665 | 0 | 1 | 0 | 0 | 1 |
| 5645 | 1 | 1 | 0 | 0 | 1 |
| 5885 | 0 | 0 | 1 | 0 | 1 |
| 5905 | 1 | 0 | 1 | 0 | 1 |
| 5925 | 0 | 1 | 1 | 0 | 1 |
| 5945 | 1 | 1 | 1 | 0 | 1 |

2 Dial-up Picture:

CH1:5740    CH2: 5760   CH3: 5780   CH4: 5800

CH5 : 5820     CH6: 5840   CH7:5860   CH8:5880

CH1:5725   CH2: 5745   CH3:5765   CH4:5785

CH5 : 5805    CH6: 5825   CH7:5845   CH8: 5865

CH1:5733   CH2: 5752    CH3: 5771   CH4: 5790

CH5:  5809   CH6: 5828   CH7: 5847   CH8:5866

CH1: 5705   CH2 :5685   CH3:5665   CH4: 5645

CH5:  5885    CH6: 5905   CH7:5925   CH8:5945

3 Receiving Antenna of Wireless Signal

- Connect the 5.8G wire(Mushroom Antenna or Panel Antenna) with the Antenna Connector

- FPV will receive signal when the signal of dial-up switch is the same with the transmitter.

4 Wiring Illustration

- Video Output Wire

5 Menu Setting

- Turn on the power switch when the power is on.

- Pressto choose Module A or B

6 Accessories

Standard Configuration：

- Sun Shade    1

- Power DC Wire  1

- AV Wire       1

- Battery Buckle   2

- 5.8G Antenna(4D)B  2（singal module:1）

选配：

- 5.8G Wire (4DB)

- 5.8G Mushroom Antenna

- 5.7G Planar Antenna

- Hot Shoe Stand

8 Main Specifications

| Screen | 7”LED |
| --- | --- |
| Resolution | 800*400 |
| Brightness | 400cd/㎡ |
| Contrast | 500：1 |
| Visual Angle | 140°/120° |
| Input Voltage | DC7-16V |
| Screen Ratio | 16：9 /4：3 |
| Current | 450mA |
| Power Dissipation | ≤6W |
| Size | 186*127*23（mm） |
| Weight | 380 |

9 Answers to the usual problems

| Break Phenomenon | Problem Analyzing |
| --- | --- |
| No picture | Check the Input power and the connceting Wire |
| Black & White Picture | Check the appropriate brightness , contrast and chroma. |

# Text boxes

2

4                           3

LIPO 3S

1 2 3 4 5 ON

OF

2

4                           3

LIPO 3S

1 2 3 4 5 ON

OF